## Slide 1: Virtual Private Networks (VPNs)

## Slide 2: What is network-layer confidentiality ?
between two network entities:
sending entity encrypts datagram payload, payload could be:
  TCP or UDP segment, ICMP message, OSPF message ….
all data sent from one entity to other would be hidden:
  web pages, e-mail, P2P file transfers, TCP SYN packets …
“blanket coverage”

## Slide 3: Virtual Private Networks (VPNs)
motivation:
institutions often want private networks for security.
  costly: separate routers, links, DNS infrastructure.
VPN: institution’s inter-office traffic is sent over public Internet instead
  encrypted before entering public Internet
  logically separate from other traffic

## Slide 4
IP
header
IPsec
header
Secure
payload
IP
header
IPsec
header
Secure
payload
IP
header
IPsec
header
Secure
payload
IP
header
payload
IP
header
payload
headquarters
branch office
salesperson in hotel
laptop
w/ IPsec
router w/
IPv4 and IPsec
router w/
IPv4 and IPsec
public Internet
Virtual Private Networks (VPNs)

## Slide 5: IPsec services
data integrity
origin authentication
replay attack prevention
confidentiality
two protocols providing different service models:
  AH
  ESP

## Slide 6: IPsec transport mode
IPsec datagram emitted and received by end-system
protects upper level protocols
IPsec
IPsec

## Slide 7: IPsec – tunneling mode
edge routers IPsec-aware
IPsec
IPsec
IPsec
IPsec
hosts IPsec-aware

## Slide 8: Two IPsec protocols
Authentication Header (AH) protocol
  provides source authentication & data integrity but not confidentiality
Encapsulation Security Protocol (ESP)
  provides source authentication, data integrity, and confidentiality
  more widely used than AH

## Slide 9: Four combinations are possible!
Host mode with AH | Host mode with ESP
Tunnel mode with AH | Tunnel mode with ESP
most common and most important

## Slide 10: Security associations (SAs)
before sending data, “security association (SA)” established from sending to receiving entity
  SAs are simplex: for only one direction
ending, receiving entitles maintain state information about SA
  recall: TCP endpoints also maintain state info
  IP is connectionless; IPsec is connection-oriented!
how many SAs in VPN w/ headquarters, branch office, and n traveling salespeople?

## Slide 11: Example SA from R1 to R2
R1 stores for SA:
32-bit SA identifier: Security Parameter Index (SPI)
origin SA interface (200.168.1.100)
destination SA interface (193.68.2.23)
type of encryption used (e.g., 3DES with CBC)
encryption key
type of integrity check used (e.g., HMAC with MD5)
authentication key
193.68.2.23
200.168.1.100
172.16.1/24
172.16.2/24
security association
Internet
headquarters
branch office
R1
R2

## Slide 12
Security Association Database (SAD)
endpoint holds SA state in security association database (SAD), where it can locate them during processing.
with n salespersons, 2 + 2n SAs in R1’s SAD
when sending IPsec datagram, R1 accesses SAD to determine how to process datagram.
when IPsec datagram arrives to R2, R2 examines SPI in IPsec datagram, indexes SAD with SPI, and processes datagram accordingly.

## Slide 13: IPsec datagram
focus for now on tunnel mode with ESP
new IP header
ESP
hdr
original IP hdr
Original IP
datagram payload
ESP
trl
ESP
auth
encrypted
“enchilada” authenticated
padding
pad length
next header
SPI
Seq
#

## Slide 14: What happens?
new IP header
ESP
hdr
original IP hdr
Original IP
datagram payload
ESP
trl
ESP
auth
encrypted
“enchilada” authenticated
padding
pad length
next header
SPI
Seq
#
193.68.2.23
200.168.1.100
172.16.1/24
172.16.2/24
security association
Internet
headquarters
branch office
R1
R2

## Slide 15: R1: convert original datagram to IPsec datagram
appends to back of original datagram (which includes original header fields!) an “ESP trailer” field.
encrypts result using algorithm & key specified by SA.
appends to front of this encrypted quantity the “ESP header, creating “enchilada”.
creates authentication MAC over the whole enchilada, using algorithm and key specified in SA;
appends MAC to back of enchilada, forming payload;
creates brand new IP header, with all the classic IPv4 header fields, which it appends before payload.

## Slide 16: Inside the enchilada:
ESP trailer: Padding for block ciphers
ESP header:
  SPI, so receiving entity knows what to do
  Sequence number, to thwart replay attacks
MAC in ESP auth field is created with shared secret key
new IP header
ESP
hdr
original IP hdr
Original IP
datagram payload
ESP
trl
ESP
auth
encrypted
“enchilada” authenticated
padding
pad length
next header
SPI
Seq
#

## Slide 17: IPsec sequence numbers
for new SA, sender initializes seq. # to 0
each time datagram is sent on SA:
  sender increments seq # counter
  places value in seq # field
goal:
  prevent attacker from sniffing and replaying a packet
  receipt of duplicate, authenticated IP packets may disrupt service
method:
  destination checks for duplicates
  doesn’t keep track of all received packets; instead uses a window

## Slide 18: Security Policy Database (SPD)
policy: For a given datagram, sending entity needs to know if it should use IPsec
needs also to know which SA to use
  may use: source and destination IP address; protocol number
info in SPD indicates “what” to do with arriving datagram
info in SAD indicates “how” to do it

## Slide 19: Summary: IPsec services
suppose Trudy sits somewhere between R1 and R2. she doesn’t know the keys.
  will Trudy be able to see original contents of datagram? How about source, dest IP address, transport protocol, application port?
  flip bits without detection?
  masquerade as R1 using R1’s IP address?
  replay a datagram?

## Slide 20: IKE: Internet Key Exchange
previous examples: manual establishment of IPsec SAs in IPsec endpoints:
    Example SA
      SPI: 12345
      Source IP: 200.168.1.100
      Dest IP: 193.68.2.23
      Protocol: ESP
      Encryption algorithm: 3DES-cbc
      HMAC algorithm: MD5
      Encryption key: 0x7aeaca…
      HMAC key:0xc0291f…
manual keying is impractical for VPN with 100s of endpoints
instead use IPsec IKE (Internet Key Exchange)

## Slide 21: IKE: PSK and PKI
authentication (prove who you are) with either
  pre-shared secret (PSK) or
  with PKI (pubic/private keys and certificates).
PSK: both sides start with secret
  run IKE to authenticate each other and to generate IPsec SAs (one in each direction), including encryption, authentication keys
PKI: both sides start with public/private key pair, certificate
  run IKE to authenticate each other, obtain IPsec SAs (one in each direction).
  similar with handshake in SSL.

## Slide 22: IKE phases
IKE has two phases
  phase 1: establish bi-directional IKE SA
    note: IKE SA different from IPsec SA
    aka ISAKMP security association
  phase 2: ISAKMP is used to securely negotiate IPsec pair of SAs
phase 1 has two modes: aggressive mode and main mode
  aggressive mode uses fewer messages
  main mode provides identity protection and is more flexible

## Slide 23: IPsec summary
IKE message exchange for algorithms, secret keys, SPI numbers
either AH or ESP protocol (or both)
  AH provides integrity, source authentication
  ESP protocol (with AH) additionally provides encryption
IPsec peers can be two end systems, two routers/firewalls, or a router/firewall and an end system