## Slide 1: Parallel Processing
Presented by:
Dr. Ashish Kumar Maurya

## Slide 2: Contents
Concurrency vs. Parallelism
Parallel Computing Platforms
Different Processor Architectures
Computing Performance
Multi-core Programming
Challenges in Multi-core Programming

## Slide 3: Concurrency vs. Parallelism
Concurrency
  Two events/threads are said to be concurrent if they occur within the same time interval
  When multiple software threads of execution are running concurrently, the execution of the threads is interleaved onto a single hardware resource
  The active threads are ready to execute, but only one thread may make progress at a given point in time

## Slide 4: Concurrency vs. Parallelism
Parallelism
  When multiple software threads of execution are running in parallel, it means that the active threads are running simultaneously on different hardware resources, or processing elements
  Multiple threads may make progress simultaneously

## Slide 5: Concurrency vs. Parallelism
Example

## Slide 6: Parallel Computing Platforms
Hardware also must supports the simultaneous execution of multiple threads.
Computer architectures can be classified by two different dimensions:
  Instruction streams
  Data Streams

## Slide 7: Parallel Computing Platforms
Flynn’s taxonomy

## Slide 8: Parallel Computing Platforms
Flynn’s taxonomy
  SISD
    Provides no parallelism in hardware
  MISD
    Generally used more as a theoretical model than a practical
  SIMD
    Useful in applications such as general digital signal processing, image processing and multimedia applications
  MIMD
    Most common parallel computing platform today eg. Intel Core Duo processor

## Slide 9: SISD

## Slide 10: SIMD

## Slide 11: MISD

## Slide 12: MIMD

## Slide 13: Different Processor Architectures
  Moore’s Law
Single-core
Multi-processor
Simultaneous Multi-Threading or SMT
Multi-core

## Slide 14: Different Processor Architectures
  Moore’s Law
  Observation, not a physical or natural law
  Guiding principles of computer architecture
  “Transistor density doubles every 18 months”
  Gordon E. Moore is co-founder of Intel
  Exponential growth
  PC costs decline
  PCs are building bricks of all future systems

## Slide 15: Different Processor Architectures

## Slide 16: Different Processor Architectures
Single core
  Has only one core or CPU in which one instruction executed at a time

## Slide 17: Different Processor Architectures
Single core

## Slide 18: Different Processor Architectures
Multi-processor
  Having two or more processing units
  Allow true parallel execution
  The tradeoff made in this case is increasing the overall system cost

## Slide 19: Different Processor Architectures
Multi-processor
  Types on the basis of processor coupling:
    Tightly coupled multi-processor
    Loosely coupled multi-processor

## Slide 20: Different Processor Architectures
Simultaneous Multi-Threading or SMT
  A physical processor is made up of a number of different resources
    including the architecture state—the general purpose CPU registers and interrupt controller registers
    caches, buses, execution units, and branch prediction logic.
  To define a thread, only the architecture state is required.
  A logical processor can thus be created by duplicating the architecture space.

## Slide 21: Different Processor Architectures
Simultaneous Multi-Threading or SMT
  SMT is a technique in which the execution resources are shared among the different logical processors.
  Issue multiple instructions from multiple threads in one cycle.

## Slide 22: Different Processor Architectures
Simultaneous Multi-Threading or SMT
  Intel’s implementation of SMT is known as Hyper-Threading Technology or HT Technology
  HT Technology literally interleaves the instructions in the execution pipeline
  HT Technology achieves performance gains through latency hiding

## Slide 23: Different Processor Architectures
Multi-core
  Next logical step from SMT
  Uses Chip Multiprocessing (CMP)
  Integrates two or more processors into one chip, each executing threads independently

## Slide 24: Different Processor Architectures
Multi-core with HT Technology
  Effectively increasing the number of logical processors by twice the number of execution cores

## Slide 25: Different Processor Architectures
Multi-core with HT Technology

## Slide 26: Different Processor Architectures
Dual-core example

## Slide 27: Computing Performance
Speedup
Amdhal’s Law
  S is the time spent executing the serial portion of the parallelized version
  N is the number of processor cores
Notes: decreasing the serialized portion by increasing the parallelized portion is of greater importance than adding more processor cores.