## Slide 1: Computer Networks
Mayank Pandey
Transport Layer

## Slide 2: Objectives
understand principles behind transport layer services:
  multiplexing/demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about transport layer protocols in the Internet:
  UDP: connectionless transport
  TCP: connection-oriented transport
  TCP congestion control

## Slide 3: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 4: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 5: Multiplexing/demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
gathering data from multiple
sockets, enveloping data with
header (later used for
demultiplexing)
Multiplexing at send host:

## Slide 6: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 7: Connectionless demultiplexing
create sockets with host-local port numbers:
DatagramSocket mySocket1 = new DatagramSocket(12534);
DatagramSocket mySocket2 = new DatagramSocket(12535);
when creating datagram to send into UDP socket, must specify
(dest IP address, dest port number)
when host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 8: Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
Client
IP:B
P2
client
IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”

## Slide 9: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 10: Connection-oriented demux (cont)
Client
IP:B
P1
client
IP: A
P1
P2
P4
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B

## Slide 11: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 12: UDP: more
often used for streaming multimedia apps
  loss tolerant
  rate sensitive
other UDP uses
  DNS
  SNMP
reliable transfer over UDP: add reliability at application layer
  application-specific error recovery!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 13: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 14: Internet Checksum Example
Note: When adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 15: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 16: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 17: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 18: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 19: Reliable data transfer: getting started
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 20: Rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver read data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 21: Rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender
How do humans recover from “errors”
during conversation?

## Slide 22: Rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender

## Slide 23: rdt2.0: FSM specification
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 24: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 25: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 26: rdt2.0 has a fatal flaw!
What happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
Handling duplicates:
sender retransmits current pkt if ACK/NAK garbled
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
Sender sends one packet,
then waits for receiver
response
stop and wait

## Slide 27: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L

## Slide 28: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 29: rdt2.1: discussion
Sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “current” pkt has 0 or 1 seq. #
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 30: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 31: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 32: rdt3.0: channels with errors and loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but use of seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 33: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L

## Slide 34: rdt3.0 in action

## Slide 35: rdt3.0 in action

## Slide 36: Performance of rdt3.0
rdt3.0 works, but performance stinks
ex: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  U sender: utilization – fraction of time sender busy sending
  if RTT=30 msec, 1KB pkt every 30 msec -> 33kB/sec thruput over 1 Gbps link
  network protocol limits use of physical resources!

## Slide 37: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 38: Pipelined protocols
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 39: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 40: Pipelined Protocols
Go-back-N: big picture:
sender can have up to N unacked packets in pipeline
rcvr only sends cumulative acks
  doesn’t ack packet if there’s a gap
sender has timer for oldest unacked packet
  if timer expires, retransmit all unack’ed packets
Selective Repeat: big pic
sender can have up to N unack’ed packets in pipeline
rcvr sends individual ack for each packet
sender maintains timer for each unacked packet
  when timer expires, retransmit only unack’ed packet

## Slide 41: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for each in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window

## Slide 42: GBN: sender extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L

## Slide 43: GBN: receiver extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK pkt with highest in-order seq #
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L

## Slide 44: GBN in action

## Slide 45: Selective Repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  again limits seq #s of sent, unACK’ed pkts

## Slide 46: Selective repeat: sender, receiver windows

## Slide 47: Selective repeat
data from above :
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 48: Selective repeat in action

## Slide 49: Selective repeat: dilemma
Example:
seq #’s: 0, 1, 2, 3
window size=3
receiver sees no difference in two scenarios!
incorrectly passes duplicate data as new in (a)
Q: what relationship between seq # size and window size?